## Slide 1
BASINFORM
Method for setting up a Programme of Measures according to EU Water Framework Directive
Dr. Bernd Klauer
MKOL, WFD, Erfurt, 7.-8. září 2006
UFZ-Umweltforschungszentrum
Leipzig-Halle GmbH
in der Helmholtz-Gemeinschaft

## Slide 2: Objectives
BASINFORM …
… structures the decision processes for the selection of measures by a management scheme,
… describes the different steps and provides the necessary evaluation methods,
… does not replace but supports decisions,
… makes decisions transparent and creates a basis for supervision and public participation
… can be flexibly adjusted to the needs of other Bundesländer and Member States,
… supports a coherent planning,
… is transferable for the entire Elbe River basin and beyond.

## Slide 3: Elements of BASINFORM
Aggregation
Identification of causes, determination of targets
Pre-selection of measures
Selection of a “best” combination of measures
Programme of Measures and River Basin Management Plan
Post-selection optimisation
Evaluation of water status
Check for exceptions
Combination of measures (Cost-effectiveness)
Check for HMWB in module “structure”
in case of HMWB
in case of less stringent environmental objectives
Consideration of baseline scenario, calculation of targets for action
Priorisation of measures
Concepts und methods
Guidance document
+
Working papers
Databank
Handbook

## Slide 4: Spatial units of river basin management according to WFD
Basic spatial unit of selection of measures: Water body or a group of water bodies.
Co-operation between Bundesländer and Member States: BASINFORM makes proposals for organisation of necessary co-ordinated actions of the different Bundesländer and Member States within the national and international river basin organisations.
  Set up of reduction targets for pollutants for up-stream and down-stream riparian states.
Elbe River basin
German part
Thuringian part
Water body or group of water bodies

## Slide 5: Five decision modules
The causes for failing the good water status are divided in five modules in order to simplify the decision making:  In each module measures can be selected independently of the selection in other modules.
Groundwater
  Module 1: Nutrients and Pesticides in groundwater
  Module 2: Other pressures on groundwater
Surface waters
  Module 3: Nutrients, organic matter and pesticides in surface waters
  Module 4: Structure and hydro morphology of surface waters
  Module 5: Other pressures on surface waters

## Slide 6: Identification of causes and determination of targets
Causes Based on the results of the monitoring and other data the causes are classified with respect to their relevance.
Catalogue of causes To simplify the work a standardised catalogue of causes is used.
Targets The environmental objective “good status” and particularly the biological components of the objective are translated for each water body into quantitative target.  Necessary for cost-effectiveness analysis
Cause
Management parameter
Development target
Target for action
P-Immissions
Target status
Total-P-concentration
Threshold concentration
Threshold load
Necessary reduction of load
Water body
State/FGG/IKSE/LAWA/EU

## Slide 7: Example for catalogue of causes
Causes | Management parameter | Unit | Develop-ment target
Module 1: Nutrients and pesticides in groundwater |  |  | 
Nitrate immissions | Concentration Total N (90 percentile) | mg/l | 50
Pesticide immissions | … | … | …
Module 2: Other pressures of groundwater |  |  | 
Groundwater abstraction | Amount of abstraction or GW-recharge minus abstraction | m3/a | regional
Salt immissions | Concentrations of different salts | … | …
Priority substances | Concentration of the different priority substances | … | …
Module 3: Nutrients, organic matter and pesticides in surface waters |  |  | 
Immissions of organic matter | BSB5 | mg/l | 4 or 6
 | NH4-N | mg/l | 0,3
Phosphate immissions | Concentration (90 Percentile) | mg/l | 0,15
Nitrate immissions | Concentration (90 Percentile) | mg/l | 3
Immissions of pesticides | Concentration different pesticides | … | …
Module 4: Structure and hydro morphology of surface waters |  |  | 
Deficits of the river floor | … | … | ØSK 3,3
Barrier-freeness for migratory fish | … | … | individual
… | … | … | …
Module 5: Other pressures of surface waters |  |  | 
Immissions of Salts | Concentrations of different salts | … | …
… | … | … | …

## Slide 8: Determination of targets
Surface water body Zwieselbach |  |  |  |  | 
Determination of target status |  |  |  |  | 
 | Cause | Immissions of organic matter |  | Nitrate immissions | Phosphorus immissions
 | Relevance of cause with respect to the current status | Significant (B) |  | Signifc. (B) | Signific. (2)
 | Management parameter | BSB5 | NH4-N | NO3-N | Total-P
 | Development target | 4 mg/l | 0,3 mg/l | 3 mg/l | 0,15 mg/l
 | Target – character | Load | Load | Load | Load
 | Target – unit | [t/a] | [t/a] | [t/a] | [t/a]
 | Target – value | 50 | 0,8 | 100 | 4
 | Status quo value | 500 | 25,5 | 250 | 10,4
Consideration of baseline scenario etc. |  |  |  |  | 
A 1 | Baseline scenario |  |  |  | 
 | - Expected investments | 120 | 9,0 | 30 | 1
 | - Impacts of future developments | 30 | 1,5 | 10 | 0,5
A 2 | Impacts of decided groundwater measures | Results of the selection of measures for connected groundwater bodies |  |  | 
 | - Groundwater body Zwieselbach | 0 | 0 | 50 | 0
A 3 | Impacts of derivation from target for action at upstream water bodies | Results from selection of measures at the upstream water bodies |  |  | 
 | (no upstream water body existing) | - | - | - | -
Calculation of target for action |  |  |  |  | 
 | Target for action = Status quo-A1-A2-A3-target value | 300 | 7,0 | 60 | 4,9

## Slide 9: Pre-selection of measures
Pre-selection of measures
Step: Select those measures from the catalogue of measures that in principle mitigate the pressures and support reaching the good status.
2. Step: Specify these measures.

## Slide 10: Impact assessment
The impact of all pre-selected measures is estimated with respect to target for action, costs, and other criteria.  Results from modelling and expert judgements
Measure | Impact on target for action |  |  | Costs |  |  | Cost-effectiveness relation |  |  | Other impacts | 
 | Target 1 | … | Target n | Total costs | For state | Investment costs | Target 1 | … | Target n |  | 
 | [unit] | … | [unit] | [€/a] | [€/a] | [€/a] | [unit] | … | [unit] | [description] | 
M1 |  |  |  |  |  |  |  |  |  |  | 
M2 |  |  |  |  |  |  |  |  |  |  | 
… |  |  |  |  |  |  |  |  |  |  | 
Mn |  |  |  |  |  |  |  |  |  |  | 
Simplified impact table (scheme)
The impact table contains further columns, where e.g. information can be given about:
  conflicts with other measures,
  conflicts with other water uses (relevant for HMWB),
  conflicts with Flora-Fauna-Habitat Framework Directive and Strategic Environmental Planning,
  exceptions.

## Slide 11: Support from third parties
Example: Integration of Water sewage treatment concepts
Responsible sewage treatment organisation …
is requested to set up or update their plans according to the identified causes for the failing of the good status and the determined targets.
supports justification of disproportional costs - if relevant.
Competent authority …
uses their proposed measures and cost estimations.
estimates impacts of measures and compares them with targets.
gives feed-back to sewage treatment organisation.
Co-operation during the selection process rises acceptance for final decisions.

## Slide 12: Selection of measures (1)
Combining measures to bundles
Using a cost efficiency tool the single measures are combined to cost-effective bundles. If there are trade-offs between objectives or conflicts between interests, several cost-effective combinations will be proposed.
Impacts | Reduction of organic matter (BSB5) [t/a] | Organic matter cost effectiveness [T€/t] | N-Reduc-tion [t/a] | N-cost-effectiveness [T€/t] | P-Reduc-tion [t/a] | P-cost-effectiveness [T€/t] | Costs [T€/a]
Measure |  |  |  |  |  |  | 
Sewage treatment 1 | 40 | 2,5 | 20 | 5,0 | 1,5 | 66,7 | 100
Sewage treatment 2 | 0 | - | 15 | 4,7 | 1,6 | 43,8 | 70
Canal system 1 | 20 | 3,5 | 10 | 7,0 | 0,6 | 116,7 | 70
Canal system 2 | 40 | 1,5 | 20 | 3,0 | 1,4 | 42,9 | 60
Riparian buffer strips | 0 | - | 5 | 8,0 | 0,8 | 50,0 | 40
Intermediate crops | 0 | - | 20 | 6,0 | 2,2 | 54,5 | 120
Total impact | 80 | - | 40 | - | 2,9 | - | 160
Target | 70 | - | 60 | - | 4,9 | - | -

## Slide 13: Selection of measures (2)
Selection of a “best” combination of measures
From the list of cost-effective combinations a “best” combination is selected.
Criteria for the final selection may be among others
  total costs,
  distribution of costs,
  available budget,
  conflicts with other measures or water uses,
  easiness of implementation.
This combination describes the best way to reach the good status.
Exceptions, Heavily Modified Water Bodies etc.
Based on the “best” combination (its costs and conflicts) the concrete environmental objective for a water body will be determined.
Different approaches to the check for HMWB are possible.
If a less stringent environmental objective is determined the selection of measures will be modified (by modifying or omitting certain measures)
If deadlines are extended the measures that will be realised until 2015 are selected (priorisation).
First assessment whether problems with FFH-Framework Directive or Strategic Environmental Planning will occur.

## Slide 14: Aggregation
Last step: Aggregation  Use of data and databank
Data may be used for internal planning.
Appropriate aggregation of the selected measures and reached environmental objectives in lists and maps for the Programme of Measures and the River Basin Management Plan (lots of details can be omitted)
Further aggregation for other reporting and communication with politicians, stakeholders and public.

## Slide 15: Summary
BASINFORM …
… offers a framework concept for selecting measures and setting up a Programme of measures.
… is not a completed tool, ready to start.
… is a flexible concept open for adjustments and modifications.