## Slide 1: Prevention of the Deterioration of the Status of the Groundwater Bodies according the WFD Interpretation and Application according the Judgment of the Court (Grand Chamber) of 1. July 2015 (C-461/13)

## Slide 2: General Statements
The regulations for the implementation of the EU Water Framework Directive (WFD), like the WFD itself, are always related to water bodies.
The place of the assessment is always the representative measuring point of the respective WB. For GWB, several representative measuring points are usually defined. The assessment shall be based on all representative measuring points identified in the management plan.
Locally limited negative effects on water features that can not be proven / measured at the representative measuring points therefore do not violate the prohibition of deterioration, as they do not affect the entire WB or other WB.
Decisive for the assessment of whether deterioration is to be expected is, in principle, the status of the WB as documented in the valid management plan. More recent, validated data / findings (in particular in the draft of the following management plan) should be used as a supplement.

## Slide 3: Deterioration of the Quantitative Status of a GWB Analogously Use of the Term „Quality Element“ concerning GWB
Element | Sub-element | Criteria | 
Groundwater Table | water balance | The level of groundwater in the groundwater body shows that the available groundwater resource is not exceeded by the long-term annual average rate of abstraction. | Annex V Nr. 2.1.2 WRRL
 | associated surface waters | The level of groundwater is not subject to anthropogenic alterations such as would result in failure to achieve the environmental objectives for associated surface waters. | 
 |  | The level of groundwater is not subject to anthropogenic alterations such as would result in any significant diminution in the status of associated surface waters. | 
 | groundwater dependent terrestrial ecosystems | The level of groundwater is not subject to anthropogenic alterations such as would result in any significant damage to terrestrial ecosystems which depend directly on the GWB. | 
 | intrusions | The level of groundwater is not subject to anthropogenic alterations such as would result in saltwater or other intrusion | 

## Slide 4: Deterioration of the Quantitative Status of a GWB
When examining the deterioration of the quantitative status of a GWB, the impact of a project on each criterion listed in Annex V, point 2.1.2 of the WFD should be examined.
There is a deterioration in the quantitative status of a GWK as soon as at least one criterion according to Annex V Number 2.1.2 WFD is no longer met. For criteria that are not met before the project, any further negative change represents a deterioration.

## Slide 5: Deterioration of the Qualitative Status of a GWB Analogously Use of the Term „Quality Element“ concerning GWB
Element | Sub-element | Criteria | 
Concentration of Pollutants | Pollutants according to Annex I and II / Part B GWD | Compliance with GW quality standards and national thresholds or exceeding a value: Compliance with Article 4 (2c) GWD | Article 4 (2c) GD
 |  | If background value > GW quality standard / threshold value: Compliance with the individual threshold value for GWB according to Art. 3 (2) GWD (definition in the RBMP) or if a threshold value is exceeded: compliance with the conditions according to Article 4 (2c) GWD | Article 3 (2) GWD Article 4 (2c) GWD
 | Other Pollutants according to Art. 3 (1b) GWD | Compliance with the threshold value according to Art. 3 (1b) GWD (definition in the RBMP) or if a threshold value is exceeded: compliance with the conditions according to Article 4 (2c) GWD | Article 3 (1b) GWD Article 4 (2c) GWD
„or“ (alternatively) |  |  | 
Other Criteria | Anthropogenic pollutant inputs | There are no indications of anthropogenic pollutant, with changes in the electrical conductivity of salts alone not giving sufficient indication of such inputs. | Article 4 (2a) GWD
 | groundwater dependent surface waters | The groundwater quality does not result in any significant deterioration of the ecological or chemical status of surface waters and, accordingly, does not lead to a failure of the environmental objectives in the groundwater dependent surface waters. | 
 | groundwater dependent terrestrial ecosystems | The groundwater quality does not result in any significant deterioration of groundwater dependent terrestrial ecosystems | 

## Slide 6: Deterioration of the Qualitative Status of a GWB
When examining a deterioration in the qualitative status of a GWB, the impact of the project on each of the relevant pollutant (according to Article 3 GWD) should be examined. If the project can be permitted, there is no deterioration because: According to German water law, any project may only be permitted if no disadvantageous change in the GW condition is expected.
There is a deterioration in the chemical status of a GWB if, as a result of the project, at least one pollutant exceeds the relevant threshold for the GWB, unless the area criterion (Article 4 (2c (i) GWD) is met.

## Slide 7: Deterioration of the Qualitative Status of a GWB
For pollutants that already exceed the relevant threshold value and the area criterion is not met (= poor status of the GWB), any further increase in concentration that can be measured or is predicted at least at one representative measuring point represents a deterioration.
The trend (Article 5 GWD) is not a relevant component for the assessment of the status of a GWB and is therefore not part of the deterioration prohibition. The trend reversal requirement is another, independent management goal, the compliance of which must be examined in addition to the prohibition of deterioration and the requirement to achieve the environmental objectives.

## Slide 8: Deterioration of the Qualitative Status of a GWB
Initial status | Prognosis | assessment
good, because there are no indications of anthropogenic pollutant inputs, etc. | Has to regard future pollutant input: | 
 | aa) no exceedance of relevant threshold values | no deterioration
 | bb) Exceedance of a relevant threshold, but the area criterion is met | no deterioration
 | cc) Exceedance of a relevant threshold, but the area criterion is not met | deterioration
good, because relevant threshold values are not exceeded | aa) No thresholds are exceeded. | no deterioration
 | bb) Exceedance of a relevant threshold, but the area criterion is met. | no deterioration
 | cc) Exceedance of a relevant threshold, but the area criterion is met. | deterioration
good despite exceeding thresholds, because the area criterion is met | aa) further increase in pollutant concentrations, but the area criterion is still met | no deterioration
 | bb) further increase in pollutant concentrations and thereby exceeding the area criterion or violation of the other criteria | deterioration
Examples: GWB is in good chemical status initially

## Slide 9: Deterioration of the Qualitative Status of a GWB
Examples: GWB is in good chemical status initially
Initial Status | Prognosis | assessment
poor, because relevant threshold values are exceeded and area criterion is not met | aa) Further increase of the concentration of the pollutant in measuring points which already exceed the threshold value | deterioration
 | bb) first exceeding a threshold value for the pollutant, which is already exceeded in the other measuring points, in another measuring point | deterioration
 | cc) first exceeding a threshold value for another pollutant and with respect to this pollutant, the area criterion is met | no deterioration
 | dd) first exceeding a threshold value for another pollutant and with respect to this pollutant, the area criterion is not met | deterioration

## Slide 10: Exception according to Article 4 (7) WFD for GWB
The deterioration in both the quantitative and the qualitative status of groundwater is exempted under Art. 4 (7) if this deterioration is due to a change in the physical properties of an associated OWB or a change in groundwater level ,
The term of physical property of water is to be interpreted broadly, so that in addition to physical changes chemical changes are included.

## Slide 11: In General - Relevance
The significance of disadvantageous changes depends on whether a change of the status classes takes place in the subcomponents. Thus, even a minimal change can lead to the change of status class and be significant, while a disadvantageous change within the status class remains irrelevant.
For subcomponents that are already in poor status, it is possible to exclude "insignificant" negative changes, which can be measured or predicted at the representative measuring point(s), but without any actual effect.

## Slide 12: In General
Changes, insofar as they are based on natural or metrological variations, are ruled out as deterioration. These factors should therefore be taken into account in the prognosis and assessment of the changes.
Short-term, actually temporary, deterioration as a result of the implementation of the project may be disregarded, if it can be safely assumed that the previous status will revert to a short-term (timely), at the latest, until the next status assessment; otherwise, an exemption according to Art. 4 (7) is required.