## Slide 1
Groundwater status assessment
H. Prchalová a kol.
28. - 29. 5. 2018, Prague, IKSE (MKOL), GW expert group
Výzkumný ústav vodohospodářský T. G. Masaryka. v.v.i., Podbabská 2582/30, Praha 6

## Slide 2
Quantitative status
Water balance approach
Units – hydrogeological regions (groundwater body)
Proportion of realised abstractions (sum) to „natural GW sources“ – mainly base flow
Abstractions: annual data (2007 – 2012), mean and maximum annual abstractions
Base flow data: long-term annual data (50% and 80%) – period 1981 – 2010, annual data (2007 – 2012)
Groundwater Chemical and Quantitative Status Assessment –Methodology – 2nd cycle

## Slide 3
Quantitative status – Methodology – 2nd cycle

## Slide 4
Quantitative status – Methodology – 2nd cycle

## Slide 5
Quantitative status – Methodology – 2nd cycle

## Slide 6
Main gaps and uncertainties:
Base flow approach is not sufficient for all types of hydrogeological structures
Base flow data (1980 – 2010) are significantly affected by water use (abstractions, flow diversions, quantity management in reservoirs)
Missing assessment of associated surface waters and depended terrestrial ecosystems
Quantitative status – Methodology – 2nd cyclus

## Slide 7
Chemical status
Three steps approach
1st step: assessment on monitoring station level – for all pollutants (55 parameters) – different threshold values – more stringent values for associated surface waters
Old contaminated sites - specific monitoring and assessment
2nd step: assessment on working unit level (part of groundwater body) – aggregation of results of all assessed pollutants from monitoring stations + old contaminated sites
One out – all out principle for hazardous substances
3rd step: assessment on groundwater body level – based on percentages of „poor“ working units (limit – 30 or 40% of poor area
Groundwater Chemical Status Assessment –Methodology – 2nd cycle

## Slide 8
Main gaps and uncertainties:
Data about old contaminated sites are not enough reliable
Missing assessment of associated surface waters and depended terrestrial ecosystems
Missing information about specific pressures for some pollutants causing failure of status assessment
Groundwater Chemical Status Assessment –Methodology – 2nd cycle

## Slide 9
Thank you for your attentions
Výzkumný ústav vodohospodářský T. G. Masaryka, v.v.i. | Podbabská 30/ 2582, 160 00 Praha 6 | +420 220 197 111 Pobočka Brno | Mojmírovo náměstí 16, 612 00 Brno-Královo Pole | +420 541 126 311
Pobočka Ostrava | Macharova 5, 702 00 Ostrava | +420 596 134 181