## Slide 1: Less stringent environmental objectives
12 GWB with less stringent objectives for chemical status:
  2 GWB because of contaminated or abandoned industrial sites
    Definition: area of groundwater, contaminated by relevant pollutants
    Criteria of delineation: 10 times the German threshold values of insignificance (GFS)
    Reasons: technical feasibility and disproportionate cost
  10 GWB because of mining (active and remediation)
  9 GWB because of lignite ( 6 of them also for the quantitative status):
    Definition: area of groundwater, contaminated by sulphate
    area of lowered groundwater level
    Criteria of delineation: threshold value (GFS) of sulphate (240mg/l)
    Reasons: technical feasibility
  1 GWB because of uranium (old mining):
    Definition: only in 2021
    Reasons: technical feasibility and disproportionate cost

## Slide 2: Less stringent environmental objectives Contaminated Sites
No further expansion of the relevant pollutants beyond the plume that was marked out within the GWB (prohibition of deterioration).
Reduction of the areal expanse of the plumes zones (reduction of the contaminated area).
Decrease of the concentration of the pollutants within the plume (reduction of pollutant concentration).
figured as ranges of multiples of the threshold value of insignificance GFS:
blue: < threshold value of insignificance (GFS)
green: ≥ 1 ... < 10 x GFS
yellow: ≥ 10 ... < 50 x GFS
orange: ≥ 50 ... < 100 x GFS
red: ≥ 100 x GFS

## Slide 3: Less stringent environmental objectives Contaminated Sites
Area (km²)
Year

## Slide 4: Less stringent environmental objectives Lignite Mining
Quantitative Status
The maximum spatial extent of different groundwater table areas, resulting from mining activities licensed or applied for:
red: maximum drawdown (areas of currently active mining)
red with white stripes : steady but not maximum drawdown
orange: decreasing groundwater level (ongoing drawdown, areas of spreading mine)
yellow: future but not yet finished drawdown
(dewatering will take place in the future)
blue: increasing groundwater level, final groundwater table not yet reached
colourless: unaffected areas or areas with final groundwater table

## Slide 5: Less stringent environmental objectives Lignite Mining

## Slide 6: Less stringent environmental objectives Lignite Mining

## Slide 7: Less stringent environmental objectives Lignite Mining

## Slide 8: Less stringent environmental objectives Lignite Mining
Areas of the mining affected quantitative status in the groundwater body SP 2-1 (Niesky), in km² and as a percentage of the area of the whole groundwater body
maximum drawdown
increasing groundwater level, final groundwater table not yet reached
steady but not maximum drawdown
decreasing groundwater level
future but not yet finished drawdown
increasing groundwater level

## Slide 9: Less stringent environmental objectives Lignite Mining
Active mining : distribution of the actual sulphate concentration within the
cone of depression
Remediation mining: distribution of the actual and the future (prognostic) sulphate
concentration
colourless: ≤ 240 mg/l (threshold value of the German Groundwater Ordinance)
yellow: > 240 to ≤ 600 mg/l (limit of concrete aggressiveness, > 600 mg/l - attack grade 2: strong)
orange: > 600 to ≤ 1400 mg/l (Gypsum saturation in carbonic aquifers)
red: > 1400 to ≤ 3000 mg/l (limit of concrete aggressiveness, > 3.000 mg/l attack grade 3: very strong)
margenta: > 3000 mg/l

## Slide 10: Less stringent environmental objectives Lignite Mining

## Slide 11: Less stringent environmental objectives Lignite Mining

## Slide 12: Less stringent environmental objectives Lignite Mining - Sulphate

## Slide 13: Deadline extension
1 GWB with extended deadline for quantitative status:
      because of abstractions until 2021
      Reasons: technical feasibility
94 GWB with extended deadline for chemical status:
      because of contaminated or abandoned industrial sites, mining, urban run-off, agriculture, other pressures
      4 GWB until 2021
      83 GWB until 2027
      7 GWB until after 2027
      Reasons:
        technical feasibility (56 GWB)
        disproportionate cost (13 GWB)
        natural conditions (79 GWB)

## Slide 14: Extended Deadline
94 GWB with extended deadline for chemical status:
 | contaminated or abandoned industrial sites | mining | urban run-off | agriculture | other pressures
technical feasibility | 4 | 16 | 2 | 34 | 6
disproportio-nate costs | - | 1 | - | 13 | -
natural conditions | 3 | 16 | 2 | 59 | 4